## Slide 1
Chapter 3
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Chapter 3 :: Topics
Introduction
Latches and Flip-Flops
Synchronous Logic Design
Finite State Machines
Timing of Sequential Logic
Parallelism

## Slide 3
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about a circuit necessary to explain its future behavior
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops
Introduction

## Slide 4
Give sequence to events
Have memory (short-term)
Use feedback from output to input to store information
Sequential Circuits

## Slide 5
The state of a circuit influences its future behavior
State elements store state
  Bistable circuit
  SR Latch
  D Latch
  D Flip-flop
State Elements

## Slide 6
Fundamental building block of other state elements
Two outputs: Q, Q
No inputs
Bistable Circuit

## Slide 7
Consider the two possible cases:
  Q = 0:
  then Q = 0, Q = 1 (consistent)
  Q = 1:
  then Q = 1, Q = 0 (consistent)
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state
Bistable Circuit Analysis

## Slide 8
SR Latch
Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1
SR (Set/Reset) Latch

## Slide 9
  S = 1, R = 0:
  then Q = 1 and Q = 0
  S = 0, R = 1:
  then Q = 0 and Q = 1
SR Latch Analysis
1

## Slide 10
  S = 1, R = 0:
  then Q = 1 and Q = 0
  Set the output
  S = 0, R = 1:
  then Q = 0 and Q = 1
  Reset the output
SR Latch Analysis
1
1

## Slide 11
  S = 0, R = 0:
  then Q = Qprev
  S = 1, R = 1:
  then Q = 0, Q = 0
SR Latch Analysis
1

## Slide 12
  S = 0, R = 0:
  then Q = Qprev
  Memory!
  S = 1, R = 1:
  then Q = 0, Q = 0
  Invalid State
  Q ≠ NOT Q
SR Latch Analysis
1

## Slide 13
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1
  (S = 1, R = 0, Q = 1)
  Reset: Make the output 0
  (S = 0, R = 1, Q = 0)
Must do something to avoid
invalid state (when S = R = 1)
SR Latch Symbol

## Slide 14
How to avoid S=1, R=1 in SR Latch Internal Circuit
Can the following circuit avoid S=1, R=1?
Two AND gates are added before S,R; One inverter is added to create input_bar.
When Control=0, R=0, S=0
When Control =1, R= input_, S=input, S is opposite to R
Hence R=1, S=1 could be avoided

## Slide 15
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1,
  D passes through to Q (transparent)
  When CLK = 0,
  Q holds its previous value (opaque)
Avoids invalid case when
Q ≠ NOT Q
D Latch

## Slide 16
D Latch Internal Circuit

## Slide 17
D Latch Internal Circuit

## Slide 18
Inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
  Q changes only on rising edge of CLK
Called edge-triggered
Activated on the clock edge
D Flip-Flop

## Slide 19
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
D Flip-Flop Internal Circuit
L1 is called Master latch, L2 is called Slave latch

## Slide 20
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
D Flip-Flop Internal Circuit
L1 is called Master latch, L2 is called Slave latch

## Slide 21
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
  L1 is transparent
  L2 is opaque
  D passes through to N1
When CLK = 1
  L2 is transparent
  L1 is opaque
  N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 1)
  D passes through to Q
D Flip-Flop Internal Circuit
L1 is called Master latch, L2 is called Slave latch

## Slide 22
D Latch vs. D Flip-Flop
Latch symbol
Flip flop symbol
CLK

## Slide 23
D Latch vs. D Flip-Flop
In latch, when CLK=1, Q=D, output Q will follow the input D when CLK=1; when CLK=0, output keeps the previous value;
Latch
CLK=1
0
Assume two different initial values: 0, 1
0
1
D changes
CLK=0

## Slide 24
D Latch vs. D Flip-Flop
In flip-flop, Q only copies D at CLK rising edge; in the other times, Q keeps previous value
Assume two different initial values: 0, 1
0
1
D value at clock edge
CL
CLK rising edge
Flip-flop
0
1
1

## Slide 25
D Latch vs. D Flip-Flop
In latch, when CLK=1, Q=D, output Q will follow the input D when CLK=1; when CLK=0, output keeps the previous value;
In flip-flop, Q only copies D at CLK rising edge; in the other times, Q keeps previous value
Flip-flop
Latch
1
0
Assume two different initial values: 0, 1
0
1

## Slide 26
Flip flop is edge-triggered (specifically only on the rising edge for the previous example; Q = D on those rising edges and Q=Qprev otherwise)
Latch is level-sensitive (if clock is high, Q = D. Otherwise, Q = Qprev)

## Slide 27
Registers: Multi-bit Flip-Flop
Registers are a group of flip fops sharing the same CLK
All bits are updated at the same time.
Registers are the key building block of most sequential circuits
The symbol of a 4 bit register is in the slide
If you have a 4 bit data D3:0: D3, D2, D1, D0, you can use a 4 bit register to store that data

## Slide 28
Appendix

## Slide 29
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state
Enabled Flip-Flops

## Slide 30
Inputs: CLK, D, Reset
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Resettable Flip-Flops

## Slide 31
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?
Resettable Flip-Flops

## Slide 32
Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop
Synchronously resettable flip-flop?

## Slide 33
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves as ordinary D flip-flop
Settable Flip-Flops